## Slide 1: THG Simulations
Code handover
21/08/2023
David Amorim

## Slide 2: Basic code flow
“file_prepare.py”
e.g., COMSOL density simulations, measured UV spectra,….
raw input data
processed input data
“THG_sim_main.jl”
output data (processed)
single run
output data (raw)
pressure scan
“scan_eval.py”

## Slide 3: General notes
The latest version of the code can be found on GitHub (now public):
  https://github.com/2538354a/Simulating-THG-of-few-femtosecond-pulses-in-a-noble-gas-
All code files are extensively commented
All relevant settings and parameters can be set at the top of each file
All files will run directly upon execution, without having to add function calls or command-line arguments
The simulation output (both raw data and plots) of previous rounds of runs and pressure scans is on Sync&Share as well as GitHub

## Slide 4: The directory structure
The default directory structure (directories in italics, code files in blue) is:
  THG_sim_main.jl
  file_prepare.py
  scan_eval.py
  input
  output
  raw_input
  scan_analysis
By default:
  file_prepare.py reads files from raw_input, processes them and stores the results in input
  THG_sim_main.jl reads from input and stores simulation data in output
  scan_eval.py reads from output and writes to scan_analysis
It can be convenient to add additional directories to store output (especially for parameter scans) in order to declutter the output directory

## Slide 5: Handling input data: “file_prepare.py”
Four different types of input files can be read in:
  UV spectra
  IR spectra
  IR time-intensity data
  Density data
file_prepare.py can be used to process these files for use in the main program (e.g. removing comments or changing delimiters)
It reads the raw input files from some directory (default: raw_input) and saves processed versions in the same directory used by the main program to read input (default: input)
file_prepare.py only needs to be used if new raw input files are to be processed and added to the input directory
The program is short, simple and easily modifiable

## Slide 6: The main file: “THG_sim_main.jl”
This is a long file but it is commented extensively and has a clear structure (with section headings):
  Set input parameters [roughly: lines 1-100]
  Feed parameters into Luna and run simulation [roughly lines 100-200]
  Process simulation output [roughly lines 200-300]
  Generate plots [roughly lines 300-600]
  Saving and writing to file [roughly lines 600-700]
To generate simulations, generally only a few variables in at the top of the file need to be changed
The following two slides explain the basic usage of the file but do not cover much of the logic behind the code

## Slide 7: The main file: “THG_sim_main.jl”
Basic usage & settings
Simulations can either be generated as single runs or as part of a pressure scan
  the output of a single run is stored in a new directory in the output directory
  for a pressure scan, a separate directory in the output directory is created for each run in the scan
  pressure scans are implemented as looped single runs with some additional constraints
  the Boolean p_scan is used to toggle between these two modes
Unless saving is explicitly turned off (save==false) there is always some saved output resulting from a single run
  the file params.txt contains a record of all relevant input parameters as well as some output parameters, like the UV pulse energy
  the file UV_spectrum.txt contains the UV spectrum written to file
  unless the txt_only setting is used, a variety of plots will be generated, shown and saved
  the setting show==false can be used to stop plots from opening in the GUI
For pressure scans the options save==false and txt_only==true are mandatory: the output of a pressure scan consists of saved text files
  the UV spectrum for each pressure is saved in an appropriately named XXbar.dat text file, where XX is the pressure in bar
  a slightly simplified version of params.txt is saved
  a file energy_efficiency_tau_zpeak.text contains the UV energy and other important variables for each pressure (1st col: pressure [bar]; 2nd col: energy [J]; 3rd col: efficiency [1]; 4th col: pulse duration [s]; 5th col: UV peak position [m])

## Slide 8: The main file: “THG_sim_main.jl”
Setting physical parameters
All relevant physical parameters are controlled in the section “SET PHYSICAL PARAMETERS” at the top of the file (roughly lines 25-50)
  see the comments in the code for an explanation of each variable
  to read input data from files, use the settings read_IR, read_UV, read_ρ, etc. at the top of the file
Note: the file names for the input files are set in the section “file handling” underneath “set physical parameters”
  it is recommended to leave these file names unchanged and use file_prepare.py to produce a new file of the same name directly from the raw data when changing between various input data files

## Slide 9: Analysing scan data: “scan_eval.py”
As described earlier, the output of a pressure scan consists entirely of raw, un-analysed data
!! Will probably have to clean up “scan_eval.py” first!